Technology: Risk Assessment	Title: Mortise Machine (Hollow Chisel Type)                              OCTOBER2015

| Identify the Hazards | Who is at Risk? | What is the Harm? | Activity Taking Place | Control Measures Required | Additional Information |
| --- | --- | --- | --- | --- | --- |
| Employees and learners should be made aware of the following hazards. 1. Impact From Ejected Pieces of Wood 2. Hand, Hair or Clothing Entanglement 3. Contact From Inadvertent Starting 4. Inhalation of Dust 5. Force Used due to Blunt Chisels 6. Maintenance 7. Impact From Ejected Chuck Key/Allen Key 8. Unauthorised Use | Technology teacher, technician and students Technology teacher, technician and students Technology teacher, technician and students Technology teacher, technician and students Technology teacher, technician and students Technician Technology teacher, technician and students User | Work pieces can become loose and be ejected. Hands or clothing can become entangled with the cutting tool. Inadvertent starting whilst setting chisel or depth gauge can cause finger or hand damage. Wood dust can be inhaled and cause respiratory problems. Injury due to additional force required to machine timber. Regular maintenance will keep the machine safe for use. A chuck or allen key left in the depth gauge or chuck can be ejected towards the user if not removed. Unauthorised use. | Mortising timber Mortising timber Mortising timber Mortising timber Mortising timber Mortising timber Mortising timber | Manufacturer’s instruction guide should be followed and kept with the department for future reference. Suitable eye protection PPE must be worn at all times. The timber should be securely clamped before use. Any packing used underneath the workpiece should also be securely clamped. Long hair and loose clothing should be tied back or otherwise secured away from moving parts. No scarves to be worn. Mortise machines should be provided with; (a) a means of electrical isolation using a fused isolating switch on or adjacent to the machine, and that it is controlled by a starter incorporating overload and no-volt release; (b) a conveniently positioned and accessible, emergency stop switch (which could be the normal “off” switch) or other suitable control device that can quickly stop the machine within 10 seconds in an emergency. (c) fixed guards (removable only with the use of a tool), or alternatively interlocked guards that enclose the drive mechanisms. LEV should be provided if it is felt that wood dust is created and the user or others close by are at risk of inhaling it. General classroom ventilation can also be used if deemed effective by the department. Only sharp mortise chisels/bits should be used. Trained technicians should sharpen chisels. Students should be aware when excessive force is required when the chisel becomes blunt. The machine should be included in a planned maintenance programme that should include electrical safety tests. The key for locking the chisel/bit in the chuck should be removed before starting the machine and after the work is completed. All allen keys used to lock the depth gauge must be removed from the machine before use. The mortise machine should not be used without Technology teacher or technician supervision. Mortise machine should be hard wired with a padlocked isolator and locked off when not in use. | Reference BS 4163:2014 Mortise machines which use a chain mechanism to cut the mortise are inappropriate for school use. Suitable eye protection conforming to BS EN 166:2002 1B should be used. Use extra timber support for long lengths of timber being mortised. Extra clamps used when appropriate. Blunt mortise chisels/drills should be reported to the technician as soon as possible and withdrawn until sharpened. The mortise machine must come to a complete stop in less than 10 seconds. If not lock the machine off and report for maintenance immediately. The risk of electric shock is reduced by good maintenance and the use of double insulated machines. |

# Text boxes

This is a generic Risk Assessment that must be modified to suit your place of work. The Risk Assessment modifications should take into consideration the activity, age/stage/pupil ability, department/working environment and the experience of the teacher in charge. If Control Measures Required as described are implemented the risk is reduced to an acceptable level for mainstream students.