# Risk Assessment	Use of Pottery Kiln

| HAZARD | PERSON (S) AFFECTED | EXISTING CONTROL MEASURES |
| --- | --- | --- |
| Hot surfaces | Staff Pupils | Hot materials handled with tongs or other suitable tools Gloves providing suitable thermal protection to EN407 and protective eye wear should be worn when removing ware while the kiln is still warm. Protective eye wear to EN166 fitted with filters conforming to EN171 should be used when removing spy hole plugs to inspect cones when the kiln is hot Kilns situated in working areas should have a barrier or kiln cage |
| Fire | Staff Pupils | Detailed fire risk assessment conducted and reviewed annually Rubbish not allowed to accumulate / located in separate room / area Flammable materials are not to be stored in the kiln room Clear circulation space is maintained at all times (450mm) Co2 fire extinguisher positioned in vicinity For further information please see protocol for ‘Fire Safety’ |
| Electrocution | Staff Pupils | No access to live heating elements – interlocking device where the kiln door can not be opened before the mains supply is switched off Kiln should be installed by a competent electrician in accordance with BS7671:2001 Accessible and labelled isolation point Extension leads / multiway plugs not to be used to connect kiln Visual inspection conducted before use The electrical installation and the kiln must be regularly inspected by a properly trained competent person |
| Chemicals | Staff Pupils | Less hazardous chemicals used wherever possible Effective hand washing after using ceramic materials and chemicals All materials are properly labelled and stored, and appropriate warnings are included in the labelling Material Safety Data Sheet for substances obtained from supplier and guidance followed COSHH assessments completed for all hazardous chemicals and control measures implemented Immediate cleaning up of any spillage |
| Dust / Fume | Staff Pupils | Cleaning routines used to limit the generation of dusts Dry materials stored in sealed containers, spillages cleaned up immediately Area regularly cleaned to prevent build up of clay dust. Floors wet mopped daily Tables and surfaces to be cleaned whilst clay is damp Aprons regularly laundered Good natural ventilation (e.g. through doors / windows or extraction fan Do not use lead based glazes |
| Gas | Staff Pupils | A master isolation valve should be installed in the gas pipe supplying the kiln in a position where it can be safely operated Each kiln should have a lever-operated isolation valve on the gas control train inlet Kilns should be purged with at least 5 times their volume of air before ignition is attempted Burners should be fitted with flame safeguard devices to cut off the gas supply if the flame goes out The kiln should not be used if there are signs of combustion products leaking from the flue, eg staining of nearby surfaces Gas systems should be regularly maintained, preferably by a gas fitter employed by a Gas-Safe registered company or a specialist kiln engineer. |
| Slips and Trips | Staff Pupils | Ensure good housekeeping in the kiln room Provide wet floor signs when floor is moped Dry mop floors after spillages There should be adequate clearance between the kiln and the ceiling There should be sufficient clearance around the kiln to allow access for maintenance, servicing and free movement of air For further information please see risk assessment and protocol for ‘Slips and Trips’ |
| Manual handling | Staff Pupils | Teachers or technicians should normally load kilns Pupils carefully supervised and correct procedures for loading and unloading strictly observed Appropriate footwear worn Mechanical lifting aids available (trolleys etc) Heavy items stored at waist level For further information please see protocol for ‘Manual Handling’ |
| Safety | Staff Pupils | Kiln only to be used by competent operators Students use only under supervision Kilns should be located away from general work areas and preferably sited in a separate room or area. Written procedures on safe use and emergency procedures posted next to kiln Kiln control panel doors and covers should be kept secured in position (eg with locks, bolts or allen screws) while the kilns is in use |

#### This is a model risk assessment – you must include further control measures where applicable

Date:		Signed:				Risk rating with all control measures in place Low/Medium/High